## Slide 1: Using FX7400 / FX7500 and FX9500 GPIOs

## Slide 2
FX7400 GPIO Connections
Two optically isolated GP outputs (open drain to GND)
Two optically isolated GP inputs (5V logic level – pulled high)
+24V DC available when operating from AC power
+24V | O/P #1 | O/P #2 | GND | I/P #1 | I/P #2 | GND
1 | 2 | 3 | 4 | 5 | 6 | 7
GPIO CONNECTOR PINOUTS

## Slide 3
MOTION SENSOR 1
FX7400 - Typical setup with light stack and motion sensors (AC power)
+24V | DOUT1 | DOUT2 | GND | DIN1 | DIN2 | GND
LAMP
LAMP
MOTION SENSOR 2
NC
NO
NO
NC
Note:
Lamps can be 24V incandescent or LEDs with suitable current limiting for 24V operation. LEDs require a common anode (positive) connection.
Note:
‘NC’ signifies Normally Closed contact on relay.
‘NO’ identifies Normally Open contact on relay.
Motion sensors may also be powered from +24V pin if sensors support 24V DC operation and total current drain is less than 1 Amp.
VIN
VIN
+
+
GND
GND

## Slide 4
MOTION SENSOR 1
FX7400 - Typical setup with light stack and motion sensors (PoE operation)
+24V | DOUT1 | DOUT2 | GND | DIN1 | DIN2 | GND
LAMP
LAMP
MOTION SENSOR 2
NC
NO
NO
NC
Note:
DC power supplies in the range 5V to 24V may be suitable provided that they are compatible with light stack and sensor power requirements.
Note:
‘NC’ signifies Normally Closed contact on relay.
‘NO’ identifies Normally Open contact on relay.
VIN
VIN
DC Power Supply
V+
V-
+
+
GND
GND

## Slide 5
FX9500 GPIO Connections
Four GP outputs (open collector to GND, 0.1 Amp max)
Four optically isolated GP inputs (external supply required)
GPIO CONNECTOR PINOUTS
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
DIN1/ DIN2 REF | DIN1 | DIN2 | DIN3/ DIN4 REF | DIN3 | DIN4 | GND | DOUT1 | DOUT2 | DOUT3 | DOUT4 | GND

## Slide 6
FX9500 - Typical setup with light stack and motion sensors
LAMP
LAMP
Note:
DC power supplies in the range 5V to 24V may be suitable provided that they are compatible with light stack and sensor power requirements.
Note:
‘NC’ signifies Normally Closed contact on relay.
‘NO’ identifies Normally Open contact on relay.
DC Power Supply
V+
V-
+
+
DIN1/ DIN2 REF | DIN1 | DIN2 | DIN3/ DIN4 REF | DIN3 | DIN4 | GND | DOUT1 | DOUT2 | DOUT3 | DOUT4 | GND
MOTION SENSOR 1
MOTION SENSOR 2
NC
NO
NO
NC
VIN
LAMP
+
VIN
GND
GND

## Slide 7
Pin # | Pin Name | Direction | Description
1 | +24V DC Power | O | Supplies +24V DC at up to 1 Amp
2 | GP output #1 | O | Signal for GP output #1
3 | GP output #2 | O | Signal for GP output #2
4 | GP output #3 | O | Signal for GP output #3
5 | GND | - | Ground Connection
6 | GP input #1 | I | Signal for GP input #1
7 | GP input #2 | I | Signal for GP input #2
8 | GND | - | Ground Connection
+24V | DOUT1 | DOUT2 | DOUT3 | GND | DIN1 | DIN2 | GND
FX7500 GPIO Connections

## Slide 8
MOTION SENSOR 1
FX7500 - Typical setup with light stack and motion sensors (AC power)
+24V | DOUT1 | DOUT 2 | DOUT3 | GND | DIN1 | DIN2 | GND
LAMP
LAMP
MOTION SENSOR 2
NC
NO
NO
NC
Note:
Lamps can be 24V incandescent or LEDs with suitable current limiting for 24V operation. LEDs require a common anode (positive) connection.
Note:
‘NC’ signifies Normally Closed contact on relay.
‘NO’ identifies Normally Open contact on relay.
Motion sensors may also be powered from +24V pin if sensors support 24V DC operation and total current drain is less than 1 Amp.
VIN
VIN
+
+
GND
GND
LAMP
+

## Slide 9
MOTION SENSOR 1
FX7500 - Typical setup with light stack and motion sensors (PoE operation)
+24V | DOUT1 | DOUT2 | DOUT3 | GND | DIN1 | DIN2 | GND
LAMP
LAMP
MOTION SENSOR 2
NC
NO
NO
NC
Note:
DC power supplies in the range 5V to 24V may be suitable provided that they are compatible with light stack and sensor power requirements.
Note:
‘NC’ signifies Normally Closed contact on relay.
‘NO’ identifies Normally Open contact on relay.
VIN
VIN
DC Power Supply
V+
V-
+
+
GND
GND
LAMP
+